## Slide 1: Exercise 14 Advanced Turning
Aim - as syllabus
Phase 5
Copyright Marcus Furniss 2019

## Slide 2: Why?
A steep turn produces a high rate and small radius of turn…
Collision Avoidance!

## Slide 3: Exercise 14 – Advanced Turning
To turn an A/C we need to bank the A/C
L = W
L
W
W
L
V
Additional lift required to maintain level flight
Vertical component of lift (V) is reduced – V does not equal W
A/C will descend and speed will increase
Advanced turns for C42 are over 30 up to 60 degrees of bank. Why 60deg?

## Slide 4: Exercise 14 – Advanced Turning
V
 AOA (stick back) =  Lift +  Induced Drag
More power to maintain A/S
L = W
L
W
V = W
Twice lift required in level 60deg banked turn
2 x Turn Force
HOW?
W
L
Significant wake turbulence is produced
Steep turn produces a high rate and small radius of turn
@ 60 deg, Load Factor doubles to 2g, stall speed increases by 41%...?
For C42, 41% increase in 41Kts = 58Kts
Load Factor

## Slide 5: Exercise 14 – Advanced Turning
Steep climbing turns
In a climbing turn, climb rate is significantly reduced at high bank angles (lift force is tilted to produce turning force)
Steep descending turns
In a descending turn descent rate increases significantly at high bank angles
Allow for when manoeuvring, especially at low level
Do not confuse with spiral dive – this manoeuvre is flow with steady A/S and under control
Manage Airspeed!
  Too much back pressure on stick…
  can result in low A/S with high bank angle…Stall
  Too little back pressure on stick…
  can result in nose low and A/S increasing…Spiral dive

## Slide 6
Entry
Reference point for turn exit/heading
Target A/S + level flight (80Kts)
Look out – lift wing to clear blind spot then look opposite direction round into turn
4. Roll into turn, coordinating aileron + rudder. Centralise aileron and rudder at desired bank angle to stop rolling movement and balance turn
As we roll in simultaneously;
Stick back ( AOA) to maintain height and stop nose from dropping into the turn (ref horizon, checked with VSI and Altimeter)
Increase power to maintain A/S (ASI)
opp
turn
  75 - 85 KTS
Exercise 14 – Advanced Turning
H.A.S.E.L.L. Check

## Slide 7
Exercise 14 – Advanced Turning
Side by side a/c have a different horizon perspective for left and right turns
The horizon is the primary reference for both bank and pitch
DO NOT CHASE THE INSTRUMENTS

## Slide 8
Exit
Anticipate reference point (30 deg)
Roll out of turn, coordinating aileron + rudder and simultaneously;
  Progressively reduce power as required and…
  Relax back pressure on column to attain the level flight attitude
Centralise roll and yaw inputs when wings level
Monitor | Input | Reference
Bank | Roll (Stick) | Horizon
Balance | Yaw (Rudder) | Balance Ball
Height | Pitch (Stick) | Horizon, VSI, ASI
Airspeed | Power (Throttle) | ASI
Maintain level turn
Exercise 14 – Advanced Turning

## Slide 9
Exercise 14 – Collision Avoidance Turn
Aim – simulate avoidance of an aircraft spotted at close range on a head on collision course
Maximum bank angle turn through 90 deg usually to RIGHT
Manoeuvre should be RAPID and SAFE, not necessarily ‘super accurate’

## Slide 10
The Spiral Dive
Not a descending turn – can develop from a poorly executed steep turn
Identified by;
   bank angle
   A/S
   G
Exercise 14 – Advanced Turning
Recovery
Reduce power to idle
Roll level with coordinated aileron and rudder (to get lift opposing weight)
Ease out of dive and adopt shallow climbing attitude
Adopt Full Powered Shallow Climb when A/S reduces to safe A/S
If not corrected, rapid height loss and A/S may increase above design limitations!

## Slide 11
Airmanship
H.A.S.E.L.L. - before manoeuvring
Lookout
  Opposite direction round to direction and DURING manoeuvre
  When climbing descending, above/ below/ forwards/ backwards
Orientation - capture reference before manoeuvre
Airspace/drift - down wind / above / below / congested areas
Physiological effects - Load factors – increased ‘G’ on body initially may feel strange
NO SOLO STUDENT PRACTICE
  The exercise must only be practiced with an instructor
Exercise 14 – Advanced Turning

## Slide 12: Exercise 14 Advanced Turning
Questions?