## Slide 1: Exercise 10b Stalling and Spin Avoidance
Aim - as syllabus
Phase 3
Copyright Marcus Furniss 2019

## Slide 2: The Stall
https://www.youtube.com/watch?v=WFcW5-1NP60
Watch for 40 seconds

## Slide 3: Stalling
In this exercise we will look at
  The characteristics of the fully developed stall
  How best to recover from it with minimum height loss
  How to safely enter a stall so we can practice it and hopefully avoid it inadvertently

## Slide 4: Theory – The Stall
44mph @ MTOW Ev-97, 41KTS C42
The stall occurs whenever the Critical Angle of Attack is exceeded
Fully controlled flight is not possible below this critical angle and airspeed

## Slide 5: Theory - Relative Airflow
Angle of Attack
Relative Airflow
Angle of Attack (AOA) is the angle between the chord line of the wing and the relative airflow

## Slide 6: Theory - Relative Airflow
Critical Angle
Relative Airflow
Angle of Attack (AOA) is the angle between the chord line of the wing and the relative airflow
The Critical Angle is the AOA at which the airflow over the top surface of wing stalls

## Slide 7: Relative Airflow
Relative Airflow
Critical Angle
It is possible for the aircraft to be stalled in any attitude
Relative Airflow
Critical Angle
Relative Airflow
Critical Angle

## Slide 8: The Stall
This can happen when handling mistakes are made:
Flying too slowly
  Inadvertently flying too slowly (the biggest cause!)
  Not appreciating stall speed will vary with load factor and weight carried (ie turning at too low an airspeed)
High speed stall
  Caused by pitching up abruptly at speed
Following engine failure in the climb
  If pilot is slow to correct nose high attitude/low airspeed

## Slide 9: The Stall
This can also happen due to mishandling environmental factors:
In wind shear or wind gradient;
  Most noticable the last few hundred feet above ground (…especially on 26 at Barton!)
  Can cause a sudden loss of speed to an aircraft approaching to land
  But can be anticipated and avoided using correct landing approach techniques

## Slide 10: Indications of Slow Flight
Air Speed Indicator (ASI)
  The ASI has a lag and can also be subject to errors when flying through rain
Reduced Airflow
  This is a good indication in open cockpit aircraft with pusher prop (ie Flexwing)
Noise reduction due reduced airflow
Possible nose high attitude
  Become familiar with correct pitch attitude for different power and flap setting
Pitch control position and pressure
  Control column will be aft of normal position and there will be forwards pressure as aircraft tries to return to trimmed cruise speed

## Slide 11: Indications of Slow Flight
Altered control response
  Pitch control will feel ‘nose heavy’
  Ailerons and rudder will be lighter and less effective (Mushy!)
  Note - elevator and rudder will be more responsive at high power settings due increased propeller slipstream
Balance
  High power in slow flight tends to yaw EV-97 and C42 to left due finer pitch of slipstream so more right rudder is required to maintain balance
  Yaw could lead to possible lateral instability

## Slide 12: The Incipient Stall - Indications
Aerodynamic buffet
  Shaking felt through the stick and airframe caused by airflow starting to separate
Nose heaviness
  As the airflow separates the centre of pressure moves rearwards
Lateral instability
  More airflow separation on one wing than other

## Slide 13: The Stall - Indications
Further increase in AOA leads to a fully developed stall
Decrease in lift
Increase in drag
You will feel aerodynamic buffet followed by
  Nose drop
  Possible wing drop
  Height loss

## Slide 14: Recovery from a Fully Developed Stall
Reduce angle of attack by moving stick forwards
HOW?

## Slide 15: Pitch Only Recovery (POR)
When additional power is not available
  ie full power climb, glide after engine failure
Move control column forwards to reduce AOA
  Positive but not too excessive (release back pressure)

## Slide 16: Pitch Only Recovery (POR)
When additional power is not available
  ie full power climb, glide after engine failure
Move control column forwards to reduce AOA
  Positive but not too excessive (release back pressure)
As soon as airspeed safe, raise nose appropriate attitude to minimise height loss

## Slide 17: Standard Stall Recovery (SSR)
Coordinated input allows a recovery with minimum height loss
Simultaneously
  Move control column forwards to reduce AOA
  Increase power (usually full power) – to aid acceleration with minimum height loss
As soon as airspeed safe, raise nose and adopt a full powered shallow climb

## Slide 18: Standard Stall Recovery (SSR)
This is a skill that requires practice;
Don’t raise nose too quickly otherwise a secondary stall may occur
Don’t raise nose too slowly otherwise excessive height loss will occur
If nose drops well below horizon delay power to prevent excessive height loss

## Slide 19: Wing Drop at the Stall
Un-stall the aircraft in the normal way (SSR)
During recovery
  Hold the ailerons neutral
  Apply (top) rudder to prevent further yaw towards the dropping wing
  Avoid excessive rudder input as this may cause a flick into an opposite wing drop
When aircraft has un-stalled use coordinated ailerons and rudder in the normal way to level wings and balance
Adopt a full powered shallow climb

## Slide 20: Stalling in a Turn
Occurs at higher speed that straight flight
Angle of bank may increase/reduce/stay same
Apply the Standard Stall Recovery
When aircraft has un-stalled use coordinated ailerons and rudder in the normal way to level wings and balance
Adopt a full powered shallow climb

## Slide 21: The Effect of Flaps on Stalling
With flaps extended
  The wing will now produce the same lift at a lower airspeed
  The stalling speed will be lower than without flaps
  The onset of stall will be greater due to increased drag
  Possibly more aggressive nose or wing drop
  The nose attitude will be lower at the stall than without flaps
44mph EV-97
36mph

## Slide 22: Recovery from the Stall with Flaps
Apply the Standard Stall Recovery
When raising the nose be aware of the lower nose attitude necessary to maintain a safe airspeed with flaps extended
Once a positive rate of climb is established retract flaps in stages

## Slide 23: To Enter a Wings Level Practice Stall
Select power and flaps setting to be used;
Raise the nose in relation to the horizon and hold
As airspeed reduces move stick progressively back until the stall occurs
or
Reduce power to idle and use elevator to maintain altitude until aircraft stalls
During entries to turning stalls hold off overbank as airspeed is reduced

## Slide 24: Stall Recovery Summary
No pilot input
SSR
Pitch only recovery
500’
150’
50’
A well executed standard stall recovery can be made with as little as 50 feet height loss

## Slide 25: Spin Avoidance
A spin is a condition of stalled flight in which the aircraft describes a spiral descent
Balanced flight can be difficult to maintain close to stall
If yaw is allowed to occur close to the stall a spin may develop
  The inner wing decelerates, drops increasing AOA…and stalls
  The aircraft will then yaw and roll towards the stalled wing, the nose drops and a spin is entered

## Slide 26: Spin Avoidance
In a spin an aircraft is;
  Stalled
  Rolling
  Yawing
  Pitching
  Side-slipping
  LOSING HEIGHT RAPIDLY!
The rotation in a spin can be very disorientating – watch this!
  https://www.youtube.com/watch?v=eVGtsK7vvnA
Apologies for the swearing 

## Slide 27: Spin Avoidance/Prevention
Avoid temptation to pick up a dropped wing with ailerons close to the stall
  It may have the reverse effect!
Maintain balance accurately with rudder when flying slow
  Never practice slow flight near the ground
Control airspeed accurately when turning and with flaps
  Base to final turn…the ‘Deadly’ turn!

## Slide 28: Spin Avoidance/Prevention
Recovery
  Close throttle
  Ailerons neutral (or let go of the stick!)
  Full opposite rudder to direction of spin (look directly over nose to determine direction of spin)
  PAUSE
  Stick forward until spin stops (if it hasn’t already)
  Centralise rudder
  Pull out of dive
  ‘Look straight down over the nose and push on the rudder to catch up with the world. If the world is racing away to the left, push the left rudder’ Curtis Pitts

## Slide 29: Airmanship
A
S
E
L
L
H
Height – minimum 1000 AGL
Airframe - flaps set as applicable, limit speed noted
Security – straps loose articles
Engine – Temperatures and Pressure OK, fuel level
Location – Clear of Airspace, Built up areas, Cloud
Lookout – clearing turn to see all around, above, below

## Slide 30: Exercise 10b Stalling and Spin Avoidance
Questions?